## Slide 1
Daniel Teal
Mech. Eng. & Math, UT Austin
Dr. Tomonobu Nakayama
Nano Functionality Integration Group at MANA, NIMS
Modeling Complex Random Memristor Networks

## Slide 2
Computers aren’t getting much faster.
(2D photolithographic silicon/CMOS)
Novel Electronics
quantum computing
search for new computing methods
3D circuitry
neuromorphic computing
(nanowire electronics)
photonic computing
programmable hardware (FPGA)

## Slide 3
Nanowire (NW): 1D cylinder of Ag, Si, Au...
NW-NW junction = circuit element
Nanowires for Electronics
Zhong, Z., Wang, D., Cui, Y., Bockrath, M. W., & Lieber, C. M. (2003). Nanowire Crossbar Arrays as Address Decoders for Integrated Nanosystems. Science, 302(5649), 1377–1379. https://doi.org/10.1126/science.1090899
equivalent circuit
nanowire
transistors
(1 µm scale)

## Slide 4
collection of Ag nanowires with PVP coating
model properties, understand potential
similar to neural network?
PVP@Ag Nanowire Networks
10µm x 50nm Ag
5nm PVP polymer
10 µm
image of a PVP@Ag network
schematic of
single nanowire

## Slide 5
Step 1: Create Simulation
Munroe, R. Circuit Diagram. XKCD 730.
a complete simulated network
memresistor junction model
current
filament forms
resistance decreases
no current, wait for time
filament decreases
returns to original state
equivalent circuit

## Slide 6
Step 2: Response to Constant Voltage
relative current density over time
+ V
GND
A

## Slide 7
Step 3: Resistance Decay with Time
full decay is very slow- weeks!
+ (small) V
GND
A

## Slide 8
Parameter sweep found nothing else

## Slide 9
One use: current switch
+V
0
+V
0
0
+V
0
+V
+V
0
0
+V
white indicates current flow
time
switch simulation

## Slide 10
Conclusions
Simulation predicts behavior
Junction memristor hypothesis supported
Network acts like planar memristor
Applications:
Switch for a finite state machine
Ephemeral memory: information that disappears after a week
Custom non-CMOS electronics
Planar memristance
Future work:
Attempt to control memristor parameters (decay, resistance)
Add capacitance for higher-order behavior
10 µm

## Slide 11
NIMS and MANA
National Science Foundation
  NSF grant no. OISE-1559368
National Nanotechnology Coordinated Infrastructure
PI: Dr. Tomonobu Nakayama
Nano Functionality Integration Group: Qiao Li, Adrian, Sasaya...
Dr. Lynn Rathbun and other program coordinators
Acknowledgements

## Slide 12
Junction Behavior

## Slide 13
NW-NW Junction Electrical Model

## Slide 14
Programming Environment

## Slide 15
Keithley SCS 4200
Test devices
Test Apparatus